.MT2
.MB0
.PO0
.PN0
                      Virtual Control Program Interface
         
                                 Version 1.0
                                June 12, 1989
         
                                VCPI SPONSORS
                                
                     A.I. Architects, Inc., Peabody, MA
                   Lotus Development Corp., Cambridge, MA
                   Phar Lap Software, Inc., Cambridge, MA
                            Quadram, Norcross, GA
                        Qualitas, Inc., Bethesda, MD
                Quarterdeck Office Systems, Santa Monica, CA
                     Rational Systems, Inc., Natick, MA
         
     VCPI Co-ordinators:               Phar Lap Software, Inc.
                                       (617) 661-1510
                                       Robert Moote
         
                                       Quarterdeck Office Systems
                                       (310) 392-9851
                                       Daniel Spear
         
                Copyright Phar Lap Software, Inc., 1987-1989
               Copyright Quarterdeck Office Systems, 1987-1989
         
    This specification may be duplicated provided it is reproduced in its 
               entirety, including the above copyright notice.





                 Version 1.0 Specification Revision History
         
     June 12, 1989         Final revision approved by attendees of the VCPI 
                           Developer's Conference, held at the offices of Phar 
                           Lap Software on April 25, 1989.  Attendees included 
                           the following VCPI sponsors:  A.I. Architects, 
                           Inc., Lotus Development Corporation, Phar Lap 
                           Software, Inc., Qualitas, Inc., Quarterdeck Office 
                           Systems, Rational Systems, Inc.; and the following 
                           observers:  Compaq Computer Corporation, Intel 
                           Corporation.
         
     May 8, 1989           Revision incorporating modifications agreed upon at 
                           the VCPI Developer's Conference.  This revision was 
                           distributed for approval to all conference 
                           attendees.
         
     March 31, 1989        A more detailed and explicit revision of the 
                           December 1987 specification, drafted for review at 
                           the VCPI Developer's Conference.
         
     December 21, 1987     First revision of the specification, written by 
                           Phar Lap Software, Inc., and Quarterdeck Office 
                           Systems.
         


1.0  Background
         
The Intel 80386 microprocessor has three fundamental operating modes.  Real 
mode is provided for backward compatibility with existing 8086 programs.  
Protected mode allows programs written specifically for the 80386 to take 
advantage of the larger address space available.  Virtual 8086 (V86) mode, 
like real mode, is used to run 8086 programs.  However, V86 mode runs under 
the control of a protected mode operating environment.  This provides certain 
advantages, chiefly the ability to enable the paging hardware of the 80386 and 
thus run multiple 8086 programs simultaneously, and also the ability to make 
arbitrary physical memory available within the V86 address space of an 8086 
program.  (The 80486 microprocessor provides the same architecture and 
operating modes as the 80386, thus software written for the 80386 runs without 
modification on an 80486).
         
The capabilities of the 8086 have spawned the creation of several new kinds of 
control programs that can run under MS-DOS on a 386 machine.  To date, these 
programs fall into three basic categories:  (1) protected mode run-time 
environments, which allow an application program to execute in protected mode 
under MS-DOS;  (2) EMS emulators, which use V86 mode to make all the memory on 
the machine available to 8086 programs which use EMS (Lotus/Intel/Microsoft 
Expanded Memory Specification) memory, and, (3) multitasking environments 
which use V86 mode to multitask 8086 MS-DOS programs, while still giving each 
8086 program a full 640Kb of physical memory (or more, if they use EMS 
memory).  Such multitasking environments typically run in conjunction with a 
separate EMS emulator, or implement the EMS interface as part of the 
multitasker.  For the remainder of this specification, the terms "DOS-
Extender," "EMS emulator," and "multitasker," respectively, will be used to 
refer to these program categories.
         
Since these control programs run under MS-DOS, it is desirable to make them 
compatible with each other, so that users don't have to turn off one control 
program in order to run an application under another control program.  The 
purpose of this document is to specify an interface that allows these classes 
of control programs to coexist successfully.  This interface is called the 
Virtual Control Program Interface, or VCPI.
         
2.0  Areas of Conflict
         
There are a variety of resource contention issues which must be solved to 
allow multiple 386 control programs to coexist.  The section below summarizes 
each of these issues.
         
2.1  Extended Memory Allocation
         
Because DOS only knows about memory below one MB, there is no universally used 
method in the DOS environment for allocating and freeing extended memory 
(memory above one MB).  The following existing techniques are available for 
allocating extended memory on both 80286 and 80386 PCs:
         
     1. Memory can be allocated "top down" by taking over the BIOS extended 
        memory size system call (INT 15h function 88h) and reporting less 
        extended memory available than is actually present on the machine. 
        This method allocates a contiguous block of memory starting at the top 
        of extended memory and growing downward.  See Appendix A.1 for a 
        description of top down allocation.
         
     2. Memory can be allocated "bottom-up" by taking over the PC reboot 
        interrupt (INT 19h) and installing a signature block and allocation 
        size marker in the interrupt handler, and boot block with an

______________________________________________________________________________         
     VCPI Version 1.0           June 12, 1989                      Page 1


        allocation size marker at one megabyte.  This is commonly referred to 
        as the VDISK technique, since it is the method employed by the 
        original IBM VDISK driver.  This method allocates a contiguous block 
        of memory starting at one megabyte and growing upward.  See Appendix 
        A.2 for a description of bottom-up allocation.
         
     3. If an XMS (Microsoft Extended Memory Specification) drive is 
        installed, extended memory can be allocated by making calls to the XMS 
        driver.  The XMS driver reserves extended memory for an XMS memory 
        pool using top-down allocation, and the allocates memory out of the 
        XMS memory pool.  Copies of the XMS specification may be obtained by 
        calling Microsoft at 1-800-426-9400.
         
A program that wishes to allocate extended memory must first determine what 
extended memory is free (not in use by another program).  It does this by 
calling INT 15h function 88h to obtain the top of free extended memory, and by 
checking the signature of INT 19h and the boot block at one megabyte for any 
bottom-up memory allocation, thus obtaining the bottom of free extended 
memory.
         
The program can then allocate its own chunk of extended memory, either top 
down by taking over INT 15h, or bottom-up by taking over INT 19h.  The top-down 
allocation method is preferable because it is simpler and more robust.  The 
diagram below shows an example in which three programs which use extended 
memory are installed.  Program 1 (the first program installed) allocates some 
extended memory bottom-up, program 2 allocates two chunks of memory, one 
bottom-up and one top-down, and program 3 allocates memory top-down.
         
top of    _______________________________
memory    |XXXXXXXXXXXXXXXXXXXXXXXXXXX|<=  allocated by program 2
          |XXXXXXXXXXXXXXXXXXXXXXXXXXX|    
          |---------------------------|--
          |***************************|<=  allocated by program 3
          |---------------------------|--
          |                           |<=  free extended memory
          |---------------------------|--
          |XXXXXXXXXXXXXXXXXXXXXXXXXXX|<=  allocated by program 2
          |XXXXXXXXXXXXXXXXXXXXXXXXXXX|
          |---------------------------|--
          |^^^^^^^^^^^^^^^^^^^^^^^^^^^|<=  allocated by program 1
1 MB   => |---------------------------|--
          |///////////////////////////|<=  BIOS ROM, screen, etc.
640 KB => |---------------------------|--
          |\\\\\\\\\\\\\\\\\\\\\\\\\\\|<=  DOS memory
          |___________________________|__ 

Note that only the last installed program which allocates extended memory top-
down or bottom-up (the first program in the interrupt chain for INT 15h or INT 
19h) can dynamically change its memory allocation. In the example above, only 
program 2 can dynamically modify its bottom-up memory allocation, and only 
program 3 can dynamically modify its top-down memory allocation.

______________________________________________________________________________
     VCPI Version 1.0           June 12, 1989                      Page 2


It is possible for VCPI memory, XMS memory and extended memory all to be 
available on a single PC.  (This can occur, for example, if a VCPI driver is 
installed and is given a portion of extended memory, an XMS driver is 
installed and even another chunk of extended memory, and the rest of extended 
memory is left free.)  Therefore, programs which can use extended memory may 
wish to look for all three sources of memory.  The recommended order of use of 
the different memory allocation methods is:  (1) VCPI memory, (2) XMS memory, 
and, (3) extended memory.
         
2.2  Mode Switching
         
All 386 control programs need to do some processing in protected mode, but 
also need to allow standard 8086 code (such as other applications, DOS, and 
the BIOS) to execute.  Therefore, they must switch between 80386 protected mode 
and either real mode or V86 mode.
         
If two control programs both switch between protected mode and real mode, no 
special problems are posed.  If, however, a control program switches between 
V86 mode and protected mode, it is impossible for a second control program to 
switch into protected mode.  This is because programs running in V86 mode are 
executing at the least privileged level of the 80386 processor, so system-
level operations will cause processor exceptions, which result in the first 
control program regaining control.  Thus the first control program must 
provide a method to allow subsequent control programs to switch to protected 
mode and back to V86 mode again.
         
2.3  8259A Interrupt Controller
         
The standard interrupt vectors used on the 386 PC for hardware interrupts 
IRQ0 - IRQ7 are vectors 08h - 0Fh.  Unfortunately, those vectors are also used 
by the 80386 processor for certain processor exceptions.  For this reason, 
some 386 control programs reprogram the 8259A interrupt controller chip to 
relocate IRQ0 - IRQ7 to different interrupt vectors.  Information about 
reprogramming of the 8259A must be made available to all cooperating 386 
control programs.
         
2.4  Privileged Instructions
         
When the 386 processor is executing in V86 mode, it is executing at privilege 
level 3 (the least privileged level), and privileged instructions cause an 
exception.  These include instructions which load or store 386 system 
registers, including the control registers, the debug registers, the test 
registers, GDTR, LDTR, and TR.  Access to some of these registers is needed in 
V86 mode; others only need to be modified as part of a mode switch to 
protected mode.
         
In addition, a number of instructions cause a general protection exception if 
the I/O privilege level (IOPL) is not 3 when executing in V86 mode.  These 
instructions must be made available, either by setting IOPL to 3, or by 
emulating the instructions.
         
3.0  Interface Summary
         
Many of the problems listed above occur only when one control program uses V86 
mode.  EMS emulators run in V86 mode and are widely used on 386 PCs, and an 
EMS interface is typically used or provided by multitaskers. In addition, one 
of the primary functions performed by EMS emulators is memory allocation.

______________________________________________________________________________
     VCPI Version 1.0           June 12, 1989                      Page 3


For these reasons, the VCPI interface is defined as a superset of the EMS 
version 4.0 interface (an EMS 4.0 driver must be provided underneath the VCPI 
interface; a copy of the EMS 4.0 interface specification may be obtained by 
calling Intel literature sales at 1-800-548-4725 and requesting part #300275).  
If an EMS emulator with the VCPI interface is installed, a multitasker and/or 
an arbitrary number of DOS-Extender programs which use the VCPI interface can 
be run.  Control programs which utilize the VCPI interface provided by the EMS 
emulator will be referred to as "clients" for the remainder of this document.  
The control program providing the VCPI interface (and the EMS 4.0 interface) 
will be referred to as the "server" for the remainder of this document.
         
A server is installed at boot time, and takes over a block of extended memory 
which becomes the expanded memory pool from which it allocates EMS pages.  
When the server is installed, it can be given all the extended memory on the 
computer, or extended memory can be "partitioned" into expanded memory and 
extended memory (i.e., some extended memory is taken by the server for the 
expanded memory pool, and the rest is left free, available for use by other 
programs).
         
Clients can obtain memory by making requests of the server.  Memory allocated 
though the VCPI interface comes out of the memory pool owned by the server 
(i.e., expanded memory), and must be in the physical address space of the 
computer (e.g., it must not be memory on a separate expanded memory board).  
If any extended memory is left free by the server, clients can allocate that 
extended memory in the usual way.
         
The VCPI interface is implemented with calls to functions provided by the 
server.  Calls need to be made both in V86 mode and in protected mode.  The 
V86 mode calls are implemented through the standard INT 67h EMS interface.  
The protected mode calls are made with FAR procedure calls to an entry point 
in the server.  The protected mode entry point is obtained via an 
initialization on call to the server.
         
Both the server and each client program maintain their own set of system 
tables (GDT, LDT, IDT, page tables, etc.)  Each client program must initialize 
a memory space in its page tables which is identical to a portion of the 
memory space used by the server, in order to provide a common ground for 
communication with the server.  When the client calls the server to switch to 
protected mode, the client's system tables are set up as part of the mode 
switch.  Likewise, when the client calls the server to switch back to V86 
mode, the server's system tables are set up.
         
The server must leave A20 (address line 20 on a PC) enabled at all times, in 
both V86 mode and in protected mode.

The client must always use the services of the server to switch modes. It 
should never, for example, implement its own switch back to V86 mode, because 
the server's system tables must be set up when executing in V86 mode.
         
4.0  V86 Mode Program Interface
         
The V86 mode interface is provided through the EMS interrupt (INT 67h), with 
an EMS function code in AH of DEh, and a VCPI function code in AL. (Note that 
any EMS driver which does not provide VCPI should return either code 84h (bad 
function code) for this EMS call, since it is not a defined function number 
for the LIM 4.0 EMS specification.)  If the function succeeds, AH is returned 
as zero; otherwise, there is an error code in AH. Except as noted for each 
call, all other registers are unchanged on output. 

_______________________________________________________________________________
     VCPI Version 1.0           June 12, 1989                      Page 4


If an undefined VCPI subfunction code is passed in AL, the server returns an 
either code in AH; the recommended value is 8Fh (bad subfunction code).
         
The IOPL-sensitive privileged instructions must be available in V86 mode.  
This means the server must either set the IOPL to 3, or emulate these 
instructions.  Other privileged instructions need not be emulated as part of 
the VCPI interface.  Instead, access to certain system registers is provided 
via system calls (see Section 4.4).
         
4.1  Presence Detection
         
The presence of a server which provides the VCPI interface is detected by 
first using one of the standard detection checks to see if an EMS driver is 
installed, and then making the EMS call below to check for the presence of 
VCPI.

==============================================================================         
INT 67h
AX = DE00h     VCPI Presence Detection
==============================================================================         
INPUTS:        None
-------------------------------------------------------------------------------         
OUTPUTS:       If VCPI is present:
                    AH = 0
                    BL = 0 (VCPI minor version number, in binary)
                    BH = 1 (VCPI major version number, in binary)
               If not present:
                    AH = nonzero (recommended value:  84h)
-------------------------------------------------------------------------------         
         
If the server is installed but no EMS memory has been allocated, the server 
may be executing in real mode rather than V86 mode.  The detection call should 
return success in real mode as well as V86 mode (so that it is possible to 
detect a VCPI server that is currently turned off, and also for backward 
compatibility with clients that make this call in real mode); however, for the 
rest of the VCPI interface to be enabled, the processor must be executing in 
V86 mode.  Therefore, the following VCPI detection sequence is recommended:
         
     1.  Check to see if the processor is an 80386 or 80486.
     2.  Check to see if an EMS driver is installed.
     3.  Allocate one EMS page.  This will turn on the EMS driver if it is 
         off, switching the processor to V86 mode.
     4.  Make the above VCPI detection call.
         
The EMS page allocated in step 3 must not be deallocated again until the 
client is done using the VCPI interface; otherwise, the server could turn off 
again, setting the processor back to real mode and disabling the VCPI 
interface.
         
Appendix A.3 contains a code sequence demonstrating VCPI detection.
         
4.2  Interface Initialization
         
The interface initialization process involves creating a common ground between 
the server and the client that allows them to communicate in protected mode, 
and providing any other information that the client may need to complete its
         
______________________________________________________________________________
     VCPI Version 1.0           June 12, 1989                      Page 5


own initialization.  Since the server and the client each have separate page 
tables, GDT, LDT, and IDT, in order to communicate in protected mode the 
client must set up a region in its page tables that maps memory used by the 
server, and must initialize segment descriptors in its GDT to point to code 
and data regions in the server.
         
The calls below are used to initialize the interface between the server and 
the client.
         
==============================================================================
INT 67h
AX = DE01h     Get Protected Mode Interface
==============================================================================        
INPUTS:        ES:DI = pointer to 4K page table buffer
               DS:SI = pointer to three descriptor table entries in the 
                       client's GDT, the first to be set up as the 
                       protected mode code segment in the server, and the 
                       additional two entries to be used as desired by 
                       the server when it is called in protected mode
-------------------------------------------------------------------------------         
OUTPUTS:       AH = 0
               DI = advanced to point to the first unused page table 
                    entry in the buffer (could be advanced by 4K, if 
                    server initializes entire page table)
               EBX = offset in code segment of protected mode entry point
-------------------------------------------------------------------------------         

The Get Protected Mode Interface call is used to set up a common frame of 
reference which allows the client to make calls to the server in protected 
mode.  The call initializes a page table which the client must set up as its 
0th page table.  This page table must map at least one megabyte of memory 
starting at linear address zero:  the real mode address space provided in V86 
mode.  In addition, the server can map any additional memory above one 
megabyte (up to a total of four megabytes, since there is just one page table) 
which it requires to provide the protected mode interface.  While the mappings 
for the first megabyte must be identical for both the client and the server 
(so the client will be able to set up segments to access its V86 memory from 
protected mode), memory above one megabyte can be mapped as desired by the 
server (e.g., if the server's code and data is mapped at a high address in its 
own page tables, it would simply map the same code and data just above one 
megabyte in the client's 0th page table).
         
For backward compatibility, both the server and the client must clear the 
software-defined bits (bits 9 - 11) in the page table entries it copies into 
the client's page table; all other bits should be preserved the client must 
not copy its 0th page table to a different physical page after this call is 
made.  This is so the server can always access the client's 0th page table.  
The client must never modify any bits other than the software-defined bits (9-
11) in the page table entries which are initialized by this call.
         
In addition to initializing the 0th page table, this call also fills in a GDT 
entry in the client's GDT.  This segment is used by the client when calling 
the server in protected mode.  The segment must be set up as a code segment, 
and must reside in the linear address space set up in the 0th page table by 
this call.  The entry point of the interface routine (its offset within the 
code segment) is returned in EBX.  Two additional entries in the client's GDT, 
immediately following the GDT entry for the code segment, are available to the 
server for its own use.  Typically at least one of these GDT segments is used 
by the server as a data segment.

______________________________________________________________________________
     VCPI Version 1.0           June 12, 1989                      Page 6


When the client calls the server in protected mode, it makes a FAR call to a 
USE32 segment, using the entry point provided by this call.  Since the server 
has initialized the code segment descriptor, it can, of course, set it up any 
way it desires, but it is responsible for executing a USE32 FAR return when it 
terminates, regardless of the actual use type of the code segment.  Thus, when 
the server is called in protected mode, it will have CS pointing to the code 
segment which is set up by this call.  It can obtain selectors for the two 
additional GDT entries which it set up by adding 0008h and 0010h, 
respectively, to the segment selector value in CS.  The server must preserve 
all segment registers across a protected mode VCPI call.

==============================================================================
INT 67h
AX = DE02h     Get Maximum Physical Memory Address
==============================================================================
INPUTS:        None
------------------------------------------------------------------------------
OUTPUTS:       AH = 0
               EDX = PHYSICAL address of the highest 4K memory page that 
                     could ever be allocated.
------------------------------------------------------------------------------

The Get Maximum Physical Memory Address call is used by the client to 
initialize its memory management data structures.  To do this, it may need to 
know the physical address of the highest 4K memory page that could ever be 
allocated by the Allocate 4K Page call specified below.  For backward 
compatibility, both the server and the client must mask the 12 LSBs of the 
physical page address (returned in EDX) to zero.
         
4.3  Memory Allocation Calls
         
The memory allocation calls are used to allocate and free 4K pages of memory. 
The server allocates these pages out of its EMS memory pool.  The client can 
also do its own allocation of extended memory or XMS memory, if any is 
available.

==============================================================================
INT 67h
AX = DE03h     Get Number of Free 4K Pages
===============================================================================
INPUTS:        None
-------------------------------------------------------------------------------         
OUTPUTS:       AH = 0
               EDX = number of free 4K pages
-------------------------------------------------------------------------------

This call returns the total number of 4K pages available to be allocated out 
of the server's expanded memory pool.
         
Note that this is the total amount of free memory available to all tasks on 
the system.  The client should allocate this memory only on an as needed 
basis. In addition, in a multitasking environment, this number does not 
reflect any memory restrictions placed on the client task by the multitasker.  
The client should, during initialization, use the EMS call Get Number of Pages 
(INT 67h function 3 (AH=42h)) to obtain the number of unallocated EMS pages 
available, and then limit its usage of memory allocated through the server to 
that amount.  (Note that the size of an EMS page is 16K, and the size of a 
page allocated through the VCPI interface is 4K.)

______________________________________________________________________________
     VCPI Version 1.0           June 12, 1989                      Page 7


==============================================================================
INT 67h
AX = DE04h     Allocate a 4K Page
===============================================================================         
INPUTS:        None
-------------------------------------------------------------------------------         
OUTPUTS:       If success:
                    AH = 0
                    EDX = PHYSICAL address of allocated 4K page
               If failure:
                    AH = nonzero (recommended value:  88h)
                    EDX = contents modified
-------------------------------------------------------------------------------         

This call allocates a 4K page of memory.  For backward compatibility, both the 
server and client must make the 12 LSBs of the physical page address (returned 
in EDX) to zero.  The client is responsible for freeing all memory allocated 
with this call before terminating execution.
         
==============================================================================
INT 67h
AX = DE05h     Free a 4K Page
===============================================================================         
INPUTS:        EDX = PHYSICAL address of 4K page to free
-------------------------------------------------------------------------------
OUTPUTS:       If success:
                    AH = 0
               If failure:
                    AH = nonzero (recommended value:  8Ah)
-------------------------------------------------------------------------------        

This call frees a page of memory previously allocated with subfunction 04h. 
For backward compatibility, both the server and the client must mask the 12 
LSBs of the physical page address (passed in EDX) to zero.

______________________________________________________________________________
     VCPI Version 1.0           June 12, 1989                      Page 8


==============================================================================
INT 67h
AX = DE06h     Get Physical Address of 4K Page in First Megabyte
===============================================================================         
INPUTS:        CX = page number (linear address of page SHR 12)
-------------------------------------------------------------------------------
OUTPUTS:       If success:
                    AH = 0
                    EDX = PHYSICAL address of 4K page
               If invalid page number:
                    AH = nonzero (recommended value:  8Bh)
-------------------------------------------------------------------------------         

This call returns the physical address of a 4K page in the first megabyte of 
the V86 mode linear address space.  For backward compatibility, both the 
server and the client must mask the 12 LSBs of the physical page address 
(returned in EDX) to zero.
         
This call is useful for obtaining the address of memory which is allocated and 
mapped into the first megabyte with the standard EMS calls.  While this 
information can also be extracted from the page table obtained with the Get 
Protected Mode Interface system call, that page table is a "snapshot" of the 
server's page tables at the time the system call was made, and would not have 
the correct addresses for any EMS memory mapped in after the Get Protected 
Mode Interface call was made.

4.4  System Register Access Calls
         
When executing in V86 mode, any attempt to load or store system registers 
causes a general protection exception.  The system calls below provide access 
to certain system registers in V86 mode.

===============================================================================
INT 67h
AX = DE07h     Read CR0
===============================================================================
INPUTS:        None
-------------------------------------------------------------------------------         
OUTPUTS:       AH = 0
               EBX = CR0 value
-------------------------------------------------------------------------------         
         
This call returns the current value of the CR0 register.

______________________________________________________________________________
     VCPI Version 1.0           June 12, 1989                      Page 9


===============================================================================
INT 67h
AX = DE08h     Read Debug Registers
===============================================================================
INPUTS:        ES:DI = pointer to array of 8 DWORDS, DR0 first in 
                       array, DR4 and DR5 not used
-------------------------------------------------------------------------------
OUTPUTS:       AH = 0
-------------------------------------------------------------------------------

This call stores the values of the debug registers into an array in memory. 


===============================================================================
INT 67h
AX = DE09h     Load Debug Registers
===============================================================================
INPUTS:        ES:DI = pointer to array of 8 DWORDS, DR0 first in array, 
                       DR4 and DR5 not used
-------------------------------------------------------------------------------
OUTPUTS:       AH = 0
-------------------------------------------------------------------------------
         
This function loads the debug registers with the values in the array.
         
4.5  8259A Interrupt Vector Mapping Calls
         
The default PC interrupt vector assignments for hardware interrupts are 
vectors 08h - 0Fh for interrupts IRQ0 - IRQ7, and vectors 70h - 77h for 
interrupts IRQ8 - IRQ15.  The 80386 processor uses interrupt vectors 08h - 0Fh 
for processor exceptions, which are important to 386-specific software.  
Therefore, some clients find it desirable to reprogram the 8259A interrupt 
controller to map the hardware interrupt vectors elsewhere in the interrupt 
space.  The server, as the first control program in place, is the repository 
of information on what the current vector mappings are.  Client programs 
should query the server during initialization to determine the current 
mappings. If they have been changed from the PC default mappings, the client 
is obligated not to change them again.  If they are still set to the PC 
defaults, the client can reprogram the interrupt controller and then inform 
the server what the new mappings are.

______________________________________________________________________________
     VCPI Version 1.0           June 12, 1989                      Page 10


===============================================================================
INT 67h
AX = DE0Ah     Get 8259A Interrupt Vector Mappings
===============================================================================
INPUTS:        None
-------------------------------------------------------------------------------
OUTPUTS:       AH = 0
               BX = 1st vector mapping for master 8259A (IRQ0-IRQ7)
               CX = 1st vector mapping for slave 8259A (IRQ8-IRQ15)
-------------------------------------------------------------------------------
         
This function returns the interrupt vectors generated by the 8259A interrupt 
controller chips when a hardware interrupt occurs.  If there is no slave 8259A 
to generate IRQ8-IRQ15 (because the software is running on a 386 accelerator 
card plugged into a PC or a PC/XT), then the value returned in CX is 
unspecified.
         
Note that, for programs who wish to take over hardware interrupts in V86 mode, 
other considerations may apply when executing in a multitasking environment.

===============================================================================
INT 67h
AX = DE0Bh     Set 8259A Interrupt Vector Mappings
===============================================================================
         
INPUTS:        BX = vector mapping for master 8259A (IRQ0-IRQ7)
               CX = vector mapping for slave 8259A (IRQ8-IRQ15)
               Interrupts disabled
-------------------------------------------------------------------------------         
OUTPUTS:       AH = 0
-------------------------------------------------------------------------------
         
This call is used by the client to inform the server if it remaps the 8259A 
interrupt controllers.  The client must leave interrupts disabled from the 
time it begins to reprogram the interrupt controllers until after it makes 
this function call to inform the server of the remapping.
         
Note that the server must leave interrupts disabled until after it has logged 
the vector mappings provided by the call.  In particular, it must not 
"reflect" the interrupt back to V86 mode before recording the information, in 
case there is another program in the INT 67h chain which enables interrupts.
         
If the client remaps the 8259A interrupt controller, it is responsible for 
restoring the original interrupt controller mappings when it terminates.
         
______________________________________________________________________________
     VCPI Version 1.0           June 12, 1989                      Page 11


4.6  Switch to Protected Mode
         
===============================================================================
INT 67h
AX = DE0Ch     Switch From V86 Mode to Protected Mode
===============================================================================
INPUTS:        ESI = linear address of data structure in first megabyte, 
                     containing values to load into system registers
               Interrupts disabled
-------------------------------------------------------------------------------         
OUTPUTS:       GDTR, IDTR, LDTR, TR loaded
               Interrupts disabled
               Control transferred to specified FAR entry point
               SS:ESP must have at least 16 BYTEs of space on it, and the 
                      protected mode entry point is required to set up its 
                      own stack before re-enabling interrupts
               EAX = contents modified
               ESI = contents modified
               DS, ES, FS, GS = contents modified
               All other registers unmodified
-------------------------------------------------------------------------------
         
This call switches to protected mode, sets up all the system tables for the 
client, and transfers control to the specified entry point in the client.  
Interrupts must remain disabled for the entire duration of the switch.  The 
ESI register contains a linear address of a data structure in the first 
megabyte; because the page table mappings for the first megabyte are identical 
in both the server's and the client's page tables, this address can be used by 
the server both before and after reloading the CR3 register.
         
The data structure pointed to by ESI looks like:
         
     10 (DWORD) CS:EIP too transfer control to
     0E (WORD)  selector value to load into TR
     0C (WORD)  selector value to load into LDTR
     08 (DWORD) linear address in first megabyte of 6-byte value to
                load into IDTR
     04 (DWORD) linear address in first megabyte of 6-byte value to
                load into GDTR
ESI->00 (DWORD) new value to load into CR3

Note that the server must load GDTR before loading the LDTR and TR (IDTR can 
be loaded at any time, since interrupts are disabled).  The GDTR and IDTR must 
be loaded with the 32-bit forms of the LGDT and LIDT instructions, not the 24-
bit forms provided for backward compatibility with the 80286 processor.  The 
server must clear the task busy bit in the TSS descriptor table entry in the 
client's GDT before loading TR (which must be loaded with an LTR instruction, 
not a task switch).  Note that, since the client's GDT could reside anywhere 
in the 4 GB linear address space, the TSS descriptor table entry cannot be 
modified (and the LDTR and TR registers cannot be loaded) until after CR3 is 
loaded with the client's value, and the data segment used to modify the TSS 
descriptor must have a base address of zero and a limit of 4 GB.  The server 
must not reload any segment registers after it loads the GDTR with the 
client's GDT address; note that the ability to modify GDTR and LDTR without 
reloading segment registers relies on the segment descriptor caching performed 
by the processor.  

______________________________________________________________________________
     VCPI Version 1.0           June 12, 1989                      Page 12


The server's code that implements the switch must reside in the linear region 
that was initialized with the Get Protected Mode Interface call (function 
DE01h), since that is the only linear region that is mapped identically in 
both the server's and the client's page tables.
         
When the client gets control, the stack is still set to whatever stack the 
server was using (because SS has not been reloaded, the descriptor cache 
register for SS still points to the server's stack segment).  The client must 
reload all segment registers and set up its own stack before enabling 
interrupts.  This is a requirement since an interrupt handler will attempt to 
save and restore segment registers, and the values left in the segment 
registers after the switch are not necessarily valid segments for the client.
         
5.0  Protected Mode Interface
         
The protected mode interface is a FAR entry point in the server, which is 
obtained during initialization with the Get Protected Mode Interface system 
call (INT 67h function DE01h).  The client makes a FAR call to a USE32 segment 
when it calls the server entry point, and the server must execute a USE32 FAR 
return when it terminates.
         
An EMS function code of DEh is passed in AH, and a VCPI function code is 
passed in AL.  If the function succeeds, AH is returned as zero; otherwise, 
there is an error code in AH.  Except as noted for each call, all other 
registers are unchanged on output.
         
If an undefined VCPI subfunction code is passed in AL, the server returns an 
error code in AH; the recommended value is 8Fh (bad subfunction code).
         
5.1  Memory Allocation Calls
         
The memory allocation calls are used to allocate and free 4K pages of memory 
the server allocates these pages out of its expanded memory pool.  The client 
can also do its own allocation of extended memory or XMS memory, if any is 
available.

===============================================================================
INT 67h         
AX = DE03h     Get Number of Free 4K Pages
===============================================================================
INPUTS:        None
-------------------------------------------------------------------------------
OUTPUTS:       AH = 0
               EDX = number of free 4K pages
-------------------------------------------------------------------------------
         
This call returns the total number of 4K pages available to be allocated out 
of the server's expanded memory pool.
         
Note that this is the total amount of free memory available to all tasks on 
the system.  The client should allocate this memory only on an as needed 
basis.  In addition, in a multitasking environment, this number does not 
reflect any memory restrictions placed on the client task by the multitasker.  
The client should, during initialization, use the EMS call Get Number of Pages 
(INT 67h function 3 (AH = 42h)) to obtain the number of unallocated EMS pages 
available, and then limit its usage of memory allocated through the server to 
that amount.  (Note that the size of an EMS page is 16K, and the size of a 
page allocated through the VCPI interface is 4K.)
          
______________________________________________________________________________
     VCPI Version 1.0           June 12, 1989                      Page 13


===============================================================================
INT 67h
AX = DE04h     Allocate a 4K page         
===============================================================================
INPUTS:        None
-------------------------------------------------------------------------------
OUTPUTS:       If success:
                    AH = 0
                    EDX = PHYSICAL address of allocated 4K page
               If failure:
                    AH = nonzero (recommended value:  88h)
                    EDX = contents modified
-------------------------------------------------------------------------------
         
This call allocates a 4K page of memory.  For backward compatibility, both the 
server and client must mask the 12 LSBs of the physical page address (returned 
in EDX) to zero.  The client is responsible for freeing all memory allocated 
with this call before terminating execution.


===============================================================================
INT 67h         
AX = DE05h     Free a 4K Page
===============================================================================
INPUTS:        EDX = PHYSICAL address of allocated 4K page
-------------------------------------------------------------------------------
OUTPUTS:       If success:
                    AH = 0
               If failure:
                    AH = nonzero (recommended value:  8Ah)
-------------------------------------------------------------------------------

This call frees a page of memory previously allocated with subfunction 04h. 
For backward compatibility, both the server and the client must mask the 12 
LSBs of the physical page address (passed in EDX) to zero.
         
______________________________________________________________________________
     VCPI Version 1.0           June 12, 1989                      Page 14


5.2  Switch to V86 Mode
         
===============================================================================
INT 67h
AX = DE0Ch     Switch From Protected Mode to V86 Mode
===============================================================================
INPUTS:        Top of stack looks as described below
               Interrupts disabled
               SS:ESP must be in the first megabyte of linear memory
               DS = segment selector that maps the entire linear address space 
                    that was obtained with subfunction 01h, Get Protected Mode 
                    Interface (i.e., its base address is 0, and its limit is 
                    the size of the address space obtained with the Get 
                    Protected Mode Interface call)
-------------------------------------------------------------------------------         
OUTPUTS:       GDTR, IDTR, LDTR, TR loaded with server's values
               Interrupts disabled
               Control transferred to specified FAR entry point
               SS:ESP and all segment registers loaded with values on stack
               EAX = destroyed
               All other registers unmodified
-------------------------------------------------------------------------------
         
This call switches from protected mode back to V86 mode, after setting up all 
of the server's system tables.  The top of stack looks as follows on input to 
this function:
         
         28 (DWORD) GS value
         24 (DWORD) FS value
         20 (DWORD) DS value
         1C (DWORD) ES value
         18 (DWORD) SS value
         14 (DWORD) ESP value
         10 (DWORD) reserved for EFLAGS value
         0C (DWORD) CS value
         08 (DWORD) EIP value
SS:ESP-> 00 (DWORD) return address from FAR call to USE32 segment
         
The first 8 bytes at SS:ESP are the return address pushed by the FAR CAlL 
instruction; since this call never returns, the return address is irrelevant 
and should be discarded.  It is the responsibility of the server to fill in an 
appropriate EFLAGS value (e.g., VM bit set, IOPL = 3, IF bit cleared) before 
executing the IRETD to return to V86 mode.  Interrupts must remain disabled 
for the entire duration of the switch, and the interrupt enable bit must be 
off in the EFLAGS value which is stored on the stack before executing the 
IRETD which switches back to V86 mode.  The server's code that implements the 
switch must reside in the linear region that was initialized with the Get 
Protected Mode Interface call (function DE01h), since that is the only linear 
region that is mapped identically in both the server's and the client's page 
tables.
         
If the client does any task switching, it should clear the TS bit in CR0 
before making this call.  Otherwise, the TS bit will still be set after the 
switch to V86 mode, and a floating point coprocessor instruction in V86 mode 
will cause an exception 7 trap to the server.
         
______________________________________________________________________________
     VCPI Version 1.0           June 12, 1989                      Page 15


                                 Appendix A
         
Implementation Notes
         
A.1  Top-Down Extended Memory Allocation
         
The BIOS extended memory size system call is used to determine the upper limit 
of extended memory which is not in use by other programs.  The following code 
fragment gets the physical address of one byte past the end of available 
extended memory in the EAX register:
         
     xor  eax,eax             ; clear MSBs in EAX
     mov  ah, 88h             ; get size of extended memory in KB
     int  15h
     shl  eax, 10             ; convert it address of top of memory
     add  eax, 100000h         

To allocate extended memory top down, simply install an INT 15h handler which 
passes all functions except 88h through to the previous INT 15h handler.  If 
an INT 15h function 88h call is made, return a value which reduces the size of 
extended memory by the amount of memory you wish to allocate.
         
A.2  Bottom-Up Extended Memory Allocation
         
Bottom-up extended memory allocation is not recommended, as it is more 
complicated and less versatile than top-down allocation.  However, programs 
that wish to allocate extended memory must first check to see if any other 
programs have allocated extended memory using the bottom-up technique.  Bottom-
up extended memory allocation is done by marking the amount of memory 
allocated in two locations.  If there is any extended memory on the system (if 
the BIOS call documented in Appendix A.1 does not return zero), it is 
necessary to check BOTH of these locations to see if any bottom-up extended 
memory has been allocated.  If the two locations show different amounts of 
allocated memory, the safest thing to do is terminate with an error message.  
Failing that, the larger of the two values found should be used.  The values 
may differ in the two locations because there are several programs available 
which use bottom-up allocation but which do not correctly update both 
locations, and also because the DOS PRINT command in DOS 3.3 or later wipes 
out the allocation information in one of the two locations.
         
The first location is the segment pointed at by the INT 19h vector (the reboot 
interrupt).  If an appropriate signature is present at a specific offset in 
this segment, then there is a 24-bit address of the first free byte of 
extended memory at another specific offset in the segment.  The following code 
fragment obtains the physical address of the first free byte of extended 
memory and loads it into EAX:
         
     data segment
          vdisk_sig db 'VDISK V'       ; signature string
          SIG _ LEN equ $ - vdisk_sig  ; signature string length
          SIG_VEC equ 19h              ; interrupt vector for signature
          SIG_OFFS equ 12h             ; offset of signature string in segment
          LO_OFFS equ 2Ch              ; offset of low word of 24-bit value
          HI_OFFS equ 2Eh              ; offset of high byte of 24-bit value
          data ends
                                                 
______________________________________________________________________________
     VCPI Version 1.0           June 12, 1989                      Page 16


     assume    cs:code,ds:data
     code      segment use16
         
          xor ax,ax                 ; get segment addr in ES
          mov es,ax
          mov ax,es:(SIG_VEC * 4) + 2 
          mov es,ax
         
          mov di,SIG_OFFS           ; branch of signature not present
          lea si,vdisk_sig
          mov ex,SIG_LEN
          cld
          repe cmpsb
          jne short no_alloc
         
          xor eax,eax               ; get addr of bottom of extended memory
          mov al,es:HI_OFFS         ; into EAX
          shl eax,16
          mov ax,es:LO_OFFS
          jmp short done            ; all done
         
     no_alloc:
               mov eax,100000h      ; no bottom-up memory allocated
         
     done:                          ; bottom of extended memory is now in EAX
     code ends
         
The second location to check is a boot block located at one megabyte.  The 
following C code fragment retrieves the allocation value from the boot block 
and saves it in the variable "bot_ext" (note that this code should NOT be 
executed if there is no extended memory on the system, since it attempts to 
read memory at one megabyte):
         
     long bot_ext;        /* addr of 1st free byte of extended memory */
     char buf [0x20];     /* buffers boot block */
     #define SIGOFF 0x03  /* offset of signature in boot block */
     #define SIZEOFF 0x1E /* offset of size word in boot block */
         
     /*
     * Read boot block at one megabyte by calling an assembly language 
     * routine (not shown) which either uses the BIOS block move call to 
     * read from extended memory, or does it in some other way.
     */
         
     read_ext(0x100000, buf, sizeof(buf));
         
     /*
     * Now check for the correct signature in the boot block, and if 
     * present, extract the bottom of available extended memory.
     */
         
     if (memcmp(&buf[SIGOFF], "VDISK", 5) != 0)
          bot_ext = 0x100000;
     else
     {
          bot_ext = 01;
          memcpy(&bot_ext, &buf[SIZEOFF], 2]; /* get KB addr */
          bot_ext = bot_ext << 10;            /* convert to byte addr */
         
______________________________________________________________________________
     VCPI Version 1.0           June 12, 1989                      Page 17


A.3  Sample VCPI Detection Code
         
The following code sequence should be used to detect the presence of the VCPI 
interface:
         
     data segment
     emm_name db 'EMMXXXX0',0      ; device name for EMM
     data ends
         
          assume      cs:code,ds:data
     code segment use16
     ;
     ; First check to make sure we are on an 80386 or 80486
     ;
          pushf               ; save flags
          xor ax,ax           ; try to put a zero word into flags and then
          push ax             ; get result back into AX
          popf
          pushf           
          pop ax
          and ax,0F000h       ; if high 4 bits of flags are all 1's, it's an
          cmp ax,0F000h       ; 8086/8088/80186/80188
          jne short not_386
          mov ax,0F000h       ; Now try to set the high 4 bits of the flags 
          push ax             ; and then get the result back in AX
          popf
          pushf
          pop ax
          and ax,0F000h        ; if none of the high 4 bits are set, it's an
          jz short not_386     ; 80286 -- otherwise, it's a 386 or 486
          popf                 ; restore flags
          jmp short ems_check  ; go to next check
     not_386:
          popf                 ; restore flags
          jmp no_vcpi          ; not a 386 or 486 -- VCPI not present

     ems_check:
     ;
     ; Check for EMS driver present
     ;
          lea dx,emm_name      ; open EMM device, read-only
          mov ax,3D00h
          int 21h
          jc short no_vcpi     ; branch if error
          mov bx,ax            ; get device information
          mov ax,4400h
          int 21h
          jc short no_vcpi     ; branch if error
          test dx,80h          ; branch if file (not device)
          jz short no_vcpi
          mov ax,4407h         ; check output status
          int 21h
          push ax              ; save return code from IOCTL call
          mov ah,3Eh           ; close file
          int 21h
          pop ax               ; restore IOCTL return code
          cmp al,0FFh          ; branch if status not device ready
          jne short no_vcpi
         
______________________________________________________________________________
     VCPI Version 1.0           June 12, 1989                      Page 18


     ; Now allocate an EMS page to make sure the EMS emulator is turned on.
     ; Note that we must save the handle for this allocated page and free it
     ; again eventually, although this is not shown in the code fragment.
     ;
         mov bx,1           ; allocate 1 EMS page
         mov ah,43h
         int 67h
         cmp ah,0          ; branch if error
         jne short no_vcpi
     ; save handle returned in DX to be freed later
         
     ; Now make VCPI detection call
     ;
         mov ax,0DE00h        ; is VCPI there?
         int 67h
         cmp ah,0             ; branch if not there
         jne short no_vcpi
     ; OK, the VCPI interface is present and the server is turned on.
     no_vcpi:                 ; VCPI interface not present
     code ends
         
______________________________________________________________________________
     VCPI Version 1.0           June 12, 1989                      Page 19



                                  GLOSSARY
         
4K page                  A four-kilobyte page, the page size allocated by 
                         calls to the VCPI interface.  A 4K page is always 
                         aligned on a four-kilobyte physical address boundary.
         
A20                      Address line 20.  On AT and MCA architectures, there 
                         is hardware to truncate physical addresses to 20 bits 
                         (one megabyte).  This is known as "disabling A20," and 
                         is for compatibility with 8086 programs which rely on 
                         address wraparound at one megabyte.  To use extended 
                         memory, it is necessary to "enable A20."
         
bottom-up allocation     Allocation of extended memory starting at one 
                         megabyte and growing upward.  This allocation method 
                         is used by older VDISK device drivers.

client                   A program which uses the VCPI interface 

expanded memory          Memory allocated by an EMS emulator 

extended memory          Physical memory above one megabyte.
         
EMS page                 A 16-kilobyte page, the page size allocated by calls 
                         to an EMS driver.  An EMS page is always allocated on 
                         a four-kilobyte physical address boundary.
         
real mode address space  Linear addresses below one megabyte (note that this 
                         does not necessarily correspond to physical addresses 
                         below one megabyte)

server                   A program which provides the VCPI interface
         
top-down allocation      Allocation of extended memory starting at the top of 
                         memory and growing downward.  This is the recommended 
                         technique for allocating extended memory.
         
______________________________________________________________________________
     VCPI Version 1.0           June 12, 1989                      Page 20